## Slide 1: “Wake Me Up”
Doug Gilliland

## Slide 2: Real World Situation
I wear a CPAP mask
CPAP machine runs all night
The CPAP machine is AC powered
Power fails where in live in SW PA frequently
Sometimes the power goes off and I don’t know it
Often the machine does not go back on after power returns (depends on duration of power outage)

## Slide 3: Project Idea
Create a device to monitor AC power
Device needs to wake me up when power goes off
False alarms (power off for too short a time) are OK
LEGAL NOTE: THE PROJECT CONCEPT HEREIN DOES NOT DESCRIBE A MEDICAL DEVICE

## Slide 4: Components
AC Powered
  Can use AC power as monitoring point
Battery backup
  Could use a supercap (initial cost vs maintenance)
Buzzer Alarm
Pushbutton to shut off alarm

## Slide 5: Power Scheme (First cut)
AC/12VDC wall wart
OR-Tied = diode
“Normal” AC/DC supply needs to be higher voltage then the battery supply
Typical battery choice 9V alkaline
When the AC fails, power will be taken from the battery

## Slide 6: Power Fail Detection
DC wall warts - typically 50 Khz switchers with small capacitance so relatively quick discharge
Scale 12V to somewhere in 1-5V
  5/12 ratio (max)
Precision not needed
Use resistive divider
Picked R1=22K, R2=10K
Vout = 5 * 10/(10+22) = 3.75V
Shared ground reference

## Slide 7: Prototype Platform
Would like some intelligence in the device
  Need to prototype quickly
  Use my TinyGrid85
“When all you have is a hammer everything looks like a nail” – Baruch's Observation

## Slide 8: TinyGrid85 Features
ATMEL ATTiny85 Microprocessor (or compatible 8-pin part)
Arduino Compatible (works with Arduino bootloader and Arduino IDE)
Prototyping area with power/ground connections
  Brings out all 5 I/O lines and the reset line to grid columns
  Laid out like a breadboard with vertically connected traces.
  Power and Ground horizontal connections though all columns
  Labeled (with letter numbers) for easy documentation
H1 - Jumper to select regulator or remove for ISP +5V (could be power switch connector)
H2 - ISP Download Header (ATTiny85-Programming)
AP1117 5V Power Regulator with area for heat dissipation
2.1mm Connector for AC adapter 7-9V input (could be higher)
(4) 4-40 or M3 screw holes for solid mounting
49x49 mm board - low cost of PWB manufacture in China ($15 for 10 cards shipped)

## Slide 9: TinyGrid85 Layout
ATTiny85
CPU
Reset Circuit
Optional GVS connectors
Prototyping grid
Power/Gnd
connections
5V Voltage Regulator
DC Power Jack
Power Switch
ISP Connector

## Slide 10: Mods to TinyGrid85
Need a diode between the input jack and the regulator
TinyGrid85 has both an input jack and a voltage regulator
But there is a etch on the rear side of the PCB from the input jack to the regulator
  Cut etch (XACTO knife) and add diode
Add 9V battery clip and 9V diode
Install GVS headers for switch and buzzer
Add voltage divider resistors

## Slide 11: Picking ATTiny85 pins
ISP uses D0-D2 but they can be used by functions on card as long as they are not hard wired to ground
5 Digital I/O pins, but…
  Only certain pins can be analog inputs
    Voltage divider needs to go to analog input line
  Only certain pins do PWM
    Might want to use PWM to control the buzzer

## Slide 12: Programming Wake Me
Arduino IDE doesn’t have built in support for the ATTiny85
http://land-boards.com/blwiki/index.php?title=ATTiny85-Programming
Once set up the ATTiny85 gets added as a board selection in the IDE

## Slide 13: Programming (pt 2)
Use ISP programming header
I have my own homebrew ISP programmer
Can also program from an Arduino UNO

## Slide 14: Code Design – First Pass
First validate the parts all work
Buzzer buzzes under program control
Switch can control buzzer
Power fail is detected

## Slide 15: Arduino Code – 2 Functions
“Normally” C calls main(), not the Arduino…
All Arduino code has two functions which must be provided
  setup( ) – run at start-up
  loop( ) – runs over and over from start to end
The hidden code in the Arduino environment is:
  setup()
  while (1)
  loop()

## Slide 16: Arduino Code
// WakeUp
// Hardware
const int BUZZER = 0;
const int BUTTON = 3;
void setup()
{
pinMode(BUZZER, OUTPUT);
pinMode(BUTTON, INPUT);
}
void loop()
{
int sensorValue;
int loopCount;
sensorValue = analogRead(2);
if (sensorValue < 512) // 2.5V
{
digitalWrite(BUZZER, HIGH);
for (loopCount = 0; loopCount < 100; loopCount++)
{
delay(100);
if (digitalRead(BUTTON) == 0)
loopCount = 100;
}
}
else
digitalWrite(BUZZER, LOW);
}

## Slide 17: Constants and Globals
Constants and/or globals are true in all .ino files
  C scope rules are different
// Hardware
const int BUZZER = 0;
const int BUTTON = 3;
Comments begin with //
Hardware pin numbers

## Slide 18: setup() Code
void setup(void)
{
pinMode(BUZZER, OUTPUT);
pinMode(BUTTON, INPUT);
}
Function name
No variables passed
No value returned
Configure pins

## Slide 19: loop( ) Code
Temporary variables
Read the divider
If the AC is low
Buzz the buzzer
100x100 ms loop = 10 seconds
If button is pressed
terminate loop early
Shut off the buzzer
void loop()
{
int sensorValue;
int loopCount;
sensorValue = analogRead(2);
if (sensorValue < 512) // 2.5V
{
digitalWrite(BUZZER, HIGH);
for (loopCount = 0; loopCount < 100; loopCount++)
{
delay(100);
if (digitalRead(BUTTON) == 0)
loopCount = 100;
}
}
else
digitalWrite(BUZZER, LOW);
}

## Slide 20: Demonstration
Pull the AC plug simulating power failure
Buzzer buzzes
Press switch to stop buzzer
Buzzer will stop on its own in 10 seconds if there is no switch press

## Slide 21: Kickstarter Rules
Why not just kickstarter it without making a prototype?

## Slide 22: First Article Board Layout
ISP conn.
ATTiny85
Switch
Buzzer
DC jack
5V reg
Diodes
9V clip
Ext Switch
Pwr (top)/Gnd (bottom)
Flood filled areas

## Slide 23: Next Steps
PWM control of buzzer
  Attack decay sound patterns?
  Increasingly loud?
  “Can’t wake the dead”
Battery test without wearing down battery?
Low battery level LED
Packaging?
Add other status LED?
Short buzz at power on?
Estimate BOM cost, sell price = pi * BOM cost

## Slide 24: Thoughts/Suggestions
Any thoughts or suggestions for improvement?